## Slide 1: Discussion 2
Yi-An Li

## Slide 2: Outline
Model Card
How setup a bench to get gm, av0, fT, V*
Diffusion Review

## Slide 3: Model Card – Where is it?

## Slide 4: Model Card – What’s inside? (gpdk045.scs)
Sections (corner, MOS type, R, C …)

## Slide 5: Model Card – What’s inside? (gpdk045_mos.scs)
What’s different between them.

## Slide 6: Model Card – What’s inside? (gpdk045_mos.scs)
What’s different between them.
L : 2~11u , W : 2~11u
L : 1~2u , W : 2~11u
…
L : 40n~60n , W : 120n~300n

## Slide 7: Model Card – What does bin mean?
https://www.ece.ubc.ca/~robertor/Links_files/Files/ICCAP-2008-doc/icmdl/icmdl05a11.html

## Slide 8: Bench Setup
Use an ideal opamp (VCVS) to fix drain voltage and bias Vgs.
  Given Id, the opamp will find a Vgs such that Vds equals desired value.
VCVS

## Slide 9: Bench Setup – av0, gm, fT ,Cgs
av0 : Sim vd/vg
gm : Sim id/vg
fT : Sim id/ig
Cgs : Sim vg/ig
bias

## Slide 10: Simulation Tips
V*
  Once you have gm & id
  Setup in output by equation.
How for find zero crossing freq. ?
  Use the function : “cross”
  Ex : cross(db(ifreq('ac "/NM3/D")) 0). . You will get the freq. where gain = 0
How know expressions for simulation results ?
  Mark “Add to Outputs”
  Expression will show up at output.

## Slide 11: Bench Setup – Cgs
Find
  Feed ac current to gate, and observe voltage.
  Drain & Body need to “move” with gate (by VCVS with gain =1) , otherwise Cgd and Cgb will also be included.
  Big inductor for DC-feed & big capacitor for DC-block.
How to get rid of ?
  Setup a reference cap with 1F
  ,

## Slide 12: av0, gm, fT ,Cgs
From ac simulation (previous pages)
Or from dc simulation
  Open ”Calculator” click “op”
  A window will pop up
  Click on the device.
  Select the parameter.
  The expression will shown on calculator ,ex: OP(“NM0”,”gm”)
Use as a reference to verify your result from ac sim.

## Slide 13: Diffusion Review
Diffusion
  n : electron concentration ( # of free elections/cm3)
Hw1
  Step1 : Find Q in a unit volume.